# Netlist Creation.
## Overview.
This command allows you to create the netlist file for your design.
A netlist is a file which describes electrical connections between components.
One thus finds there
- The list of the components
- The list of connections between components, called equipotential nets.
There are different netlist formats. Sometimes the component list and equipotential list are two separate files.
This netlist is fundamental in the use of schematic capture software, because the netlist is the link with other electronic CAD software, like:
- PCB software.
- Simulators.
- PAL (and other programmable IC's) compilers.

Eeschema supports several netlist formats :

- PCBNEW format (printed circuits).
- ORCAD PCB2 format (printed circuits).
- CADSTAR format (printed circuits).
- Spice format, for the simulators. ( format Spice is also used by other simulators).
## Netlist formats.
Select the tool to open the netlist creation dialog box :

Pcbnew selected
Spice selected

Using the different tabs, you can select the desired format as the default format.
In Spice format, you can generate netlists with either equipotential names (it is more legible) or net numbers (old Spice versions accept numbers only)

By clicking the Netlist button, you will be asked for a netlist file name.
Note :
With big projects, the netlist generation can take a few minutes.
## Examples.
You can see below a schematic design using the PSPICE library :

Structure of a PCBNEW netlist :

# EESchema Netlist Version 1.0 generee le 21/1/1997-16:51:15
(
(32E35B76 $noname C2 1NF {Lib=C}
(1 0)
(2 VOUT_1)
)
(32CFC454 $noname V2 AC_0.1 {Lib=VSOURCE}
(1 N-000003)
(2 0)
)
(32CFC413 $noname C1 1UF {Lib=C}
(1 INPUT_1)
(2 N-000003)
)
(32CFC337 $noname V1 DC_12V {Lib=VSOURCE}
(1 +12V)
(2 0)
)
(32CFC293 $noname R2 10K {Lib=R}
(1 INPUT_1)
(2 0)
)
(32CFC288 $noname R6 22K {Lib=R}
(1 +12V)
(2 INPUT_1)
)
(32CFC27F $noname R5 22K {Lib=R}
(1 +12V)
(2 N-000008)
)
(32CFC277 $noname R1 10K {Lib=R}
(1 N-000008)
(2 0)
)
(32CFC25A $noname R7 470 {Lib=R}
(1 EMET_1)
(2 0)
)
(32CFC254 $noname R4 1K {Lib=R}
(1 +12V)
(2 VOUT_1)
)
(32CFC24C $noname R3 1K {Lib=R}
(1 +12V)
(2 N-000006)
)
(32CFC230 $noname Q2 Q2N2222 {Lib=NPN}
(1 VOUT_1)
(2 N-000008)
(3 EMET_1)
)
(32CFC227 $noname Q1 Q2N2222 {Lib=NPN}
(1 N-000006)
(2 INPUT_1)
(3 EMET_1)
)
)
# End

In PSPICE format, the netlist is as follows:

* EESchema Netlist Version 1.1 (Spice format) creation date: 18/6/2008-08:38:03

.model Q2N2222 npn (bf=200)
.AC 10 1Meg *1.2
.DC V1 10 12 0.5

R12 /VOUT N-000003 22K
R11 +12V N-000003 100
L1 N-000003 /VOUT 100mH
R10 N-000005 N-000004 220
C3 N-000005 0 10uF
C2 N-000009 0 1nF
R8 N-000004 0 2.2K
Q3 /VOUT N-000009 N-000004 N-000004 Q2N2222
V2 N-000008 0 AC 0.1
C1 /VIN N-000008 1UF
V1 +12V 0 DC 12V
R2 /VIN 0 10K
R6 +12V /VIN 22K
R5 +12V N-000012 22K
R1 N-000012 0 10K
R7 N-000007 0 470
R4 +12V N-000009 1K
R3 +12V N-000010 1K
Q2 N-000009 N-000012 N-000007 N-000007 Q2N2222
Q1 N-000010 /VIN N-000007 N-000007 Q2N2222

.print ac v(vout)
.plot ac v(nodes) (-1,5)

.end
## Note.
### Precautions.
Many versions of software that exploit netlists do not accept spaces in the component names, pins, equipotentials or others.
Systematically avoid spaces in labels, or names and value fields of components or their pins.
In the same way, certain characters other than letters and numerals can induce problems.
Note that this limitation is not related to Eeschema, but to netlist formats that can then become untranslatable, or to software which uses these netlists.
### PSPICE netlists.
For the Pspice simulator, you have to include some command lines in the netlist itself (.PROBE, .AC…).
Any text line included in the schematic diagram starting with the keyword .-pspice or -gnucap will be inserted (without the keyword) at the top of the netlist.
Any text line included in the schematic diagram starting with the keyword .+pspice or +gnucap will be inserted (without the keyword) at the end of the netlist.

For example: if you type the following text (and not the label!):
.-PSPICE .PROBE
a line .PROBE will be inserted in the netlist.
In the previous example, three lines were inserted at the beginning of the netlist and two at the end with this technique.

Besides, also note that the equipotential GND must be named 0 (zero) for Pspice.

## Using « plugins »
For other netlist formats one can add netlist converters.
These converters are automatically launched by Eeschema
### Init the Dialog window:
One can add a new netlist plugin by « Add Plugin »

Here is the plugin « PadsPcb » setup:

The setup needs::
- A title (for instance: the name of the netlist format)
- The plugin to launch.
On activate the Netlist button: :
1. Eeschema creates an intermediate file *.tmp, for instance test.tmp
2. Eeschema run the plugin, what read test.tmp ans creates test.net
### The Plugin
this is a very simple software, because his purpose is only to convert an input text file -the intermediate text file) to an other text file.
Command created to run the plugin:
Example
F:\kicad\bin\plugins\netlist_form_pads-pcb.exe test.tmp test.net

F:\kicad\bin\plugins\netlist_form_pads-pcb.exe	Command
test.tmp	name of the input file
test.net	name of the output file

### Format of the intermediate netlist text file:
There are two sections:
1. The Components Section
2. The Nets Section
Most of known netlist formats use one or both sections, and therefore the conversion from the intermediate netlist file format to other netlist formats is usually trivial.

Here is an example (some lines from a netlist)
$BeginNetlist / $BeginComponentList / $BeginComponent / TimeStamp=456A8ACC / Footprint= / Reference=P4 / Value=CONN_2 / Libref=CONN_2 / $BeginPinList / 1=$-000002 / 2=$-000003 / $EndPinList / $EndComponent / $BeginComponent / TimeStamp=454A08DD / Footprint= / Reference=U1 / Value=ECC83 / Libref=ECC83_2 / $BeginPinList / 1=$-000005 / 2=$-000007 / 3=$-000006 / 4=$-000002 / 5=$-000002 / 6=$-000008 / 7=$-000005 / 8=$-000009 / 9=$-000003 / $EndPinList / $EndComponent / $EndComponentList	$BeginNets / Net 1 "GND" / R2 2 / R4 2 / R3 2 / P1 1 / P2 2 / P3 2 / C1 2 / Net 2 "" / U1 5 / U1 4 / P4 1 / Net 3 "" / U1 9 / P4 2 / Net 4 "" / P2 1 / C2 1 / R3 1 / $EndNets / $EndNetlist

#### la section Composant

$BeginComponentList	Beginning of the section
$EndComponentList	End of section

$BeginComponent	Beginning of a component description
TimeStamp=456A8ACC	Time stamp (Used in some netlist formats)
Footprint=	Footprint name (footprint fields of the component)
Reference=P4	Schematic reference
Value=CONN_2	Value
Libref=CONN_2	Component name in the schematic libraries (Generally not used in netlists)
$BeginPinList	Beginning of pins list
1=$-000002	<Pin num> = <net name>
2=$-000003	<Pin num> = <net name>
$EndPinList	End of pins list
$EndComponent	End of a component description

#### la section Nets
$BeginNets	Beginning of the section
Net 1 "GND"	Net <net number> <net name>
R2 2	<component reference> <pin number>
R4 2
R3 2
P1 1
P2 2
P3 2
C1 2
Net 2 ""	Net <net number> <net name> (iNo net name here)
U1 5
U1 4
P4 1
$EndNets	End of section

Here is a conversion to pads pcb:
*PADS-PCB*
*PART*
P4 unknown
U1 unknown
C1 unknown
P3 unknown
P2 unknown
P1 unknown
C2 unknown
R3 unknown
R4 unknown
R2 unknown
R1 unknown

*NET*
*SIGNAL* GND
 R2.2
 R4.2
 R3.2
 P1.1
 P2.2
 P3.2
 C1.2
*SIGNAL* N-000002
 U1.5
 U1.4
 P4.1
*SIGNAL* N-000003
 U1.9
 P4.2

This format is an easy conversion of sections found in the intermediate file.

postamble();