# Creating the copper zones
Copper zones are defined by an outline (closed polygon), and can include holes (closed polygons inside the outline).
Pcbnew uses currently track segments to fill copper areas.
Copper zones must be filled or refilled when all the routing is finished.

Pads of the net must be already connected by standard tracks.
Do not expect connecting pads through the zone because the DRC does not test zones to evaluate the pad connexions (because of time computation problems).

Copper zones (Usually ground and power planes) are usually attached to a net.
In order to create a copper zone one must:
- Select parameters (net name, layer ...)
  Switch on the layer and highlight this net is not mandatory but is a good practice.
- Create the zone limit (If no, All the board will be filled.)
- Fill the zone.
Pcbnew try to fill zones all of a piece, and usually, there is not any unconnected copper block. So it can happens some fragments of areas remain not filled.
## Net selection:
Use the tool , and click on a pad connected to the net, which must be highligted.
## Creating a zone:
### Creating the zone limits:
Use the tool .
Choose the layer for the zone.
When clicking to start the zone outline, the dialog box is opened:

On can set parameters for this zone (net, layer, filling grid, pad options ...)
Draw the zone limit, on this layer.
This zone limit is a polygon, created by a click (left button) for each corner.
A double click ends the polygon.
The polygon will be automatically closed. If the starting point and the ending point are not at the same coordinate, Pcbnew will add a segment from the end point to the start point.
Remark:
- The DRC control is active when creating zone outlines.
- A corner which creates a DRC error will NOT be accepted by Pcbnew.

Here is a zone limit created (polygon in thin hatched line):

### Filling the zone:
The filling zone is initiated from starting points : pads, track ends.
If Pcbnew does not find a staring point, it cannot fill the zone.
To test the zone filling, right click on the edge zone::

Activate the "Fill Zone" command
Here is the filling result for a starting point inside the polygon:

r

The polygon is a frontier for filling.
One can see a non filled area inside the zone, because this area is not accessible:
- A track creates a frontier and
- There is no starting point for filling in this area.

Note:
you can use many polygons to create cutout areas. Here is an example:

Here is the result:

## Fill Options:

One must choose:
- The working grid for filling.
- The clearance.
- How the pads are drawn inside the zone (or connected to this zone).
### Working grid for filling.
The smaller the filling grid is, the better the filling is.
However, the filling is made with horizontal and vertical track segments, if the grid is small, board files can be very larges (several Mo.).
A 0.01 inch grid is a good compromise.
### Clearance
A good choice is a grid a bit bigger than the routing grid.
### Pad options
Pads of the net can either be included or excluded from the zone, or connected by thermal reliefs.
- If included, soldering and unsoldering can be very difficult.
- If excluded, the connection to the zone is not very good.
- A thermal relief is a good compromise.

Here is the result for the 3 options:

Include Pads
Exclude Pads
Thermal relief. / Pad is connected by 4 track segments. / The segment width is the current value used for the track width.

## Adding a Cutout area inside a zone:
Obviously, a zone must already exist.
To add a cutout area (a non filled area inside the zone):
- Right click on an existing edge outline.
- Select Add Cutout Area.
- Creates the new outline.

After creating outline:
See the cutout outline.

## Outlines editing:
An outline can be modified by:
- Moving a corner or an edge
- Deleting or Adding a corner
- Adding a similar zone, or a cutout area
And if polygons are overlapping they will be combined.

To do that:
Right click on a corner or on an edge, en select the command.

Here is a corner (from a cutout) moving:

Here is the result:

Polygons are combined.

Adding a similar zone:
Adding the zone
Result

## Editing zone: parameters
When right clicking on an outline, and using Edit Zone Params , The Zone params Dialog box is opened.
Inital parameters can be edited.
If the zone is already filled, refilling it will be necessary.
## Final zone Filling.
When the board is finished, one must fill or refill all zones.
To do that:
- Activate the tool zones ().
- Right click to display the Popup menu.
- Use Fill or Refill All Zones

Warning, calculations can take some time, if filling grid is small.
## Zones net names changes:
After editing a schematic, nets can have their name changed.
For instance VCC can be changed to +5V.
When a global DRC control is made Pcbnew checks if the zone net name exists, and displays an error if not.
A "by hand" parameter zone edition will be necessary to change the old name to the new one.