# Customize Netlists and BOM

## The Intermediate Netlist:
BOM and netlists can be converted from an Intermediate Netlist file created by Eeschema.
This file uses an XML syntax.
This file is called Intermediate Netlist.
But because it includes a lot of data about components, it can also be used to create BOM or others reports, not just netlists.
Depending on the output (BOM, new netlist), only some of sections in this Intermediate Netlist will be used.
Here is a sample:

### Schematic sample:

### The Intermediate Netlist file sample:
The corresponding intermediate netlist (using XML syntax) is:

<?xml version="1.0" encoding="utf-8"?>
<export version="D">
  <design>
    <source>F:\kicad_aux\netlist_test\netlist_test.sch</source>
    <date>29/08/2010 20:35:21</date>
    <tool>eeschema (2010-08-28 BZR 2458)-unstable</tool>
  </design>
  <components>
    <comp ref="P1">
      <value>CONN_4</value>
      <libsource lib="conn" part="CONN_4"/>
      <sheetpath names="/" tstamps="/"/>
      <tstamp>4C6E2141</tstamp>
    </comp>
    <comp ref="U2">
      <value>74LS74</value>
      <libsource lib="74xx" part="74LS74"/>
      <sheetpath names="/" tstamps="/"/>
      <tstamp>4C6E20BA</tstamp>
    </comp>
    <comp ref="U1">
      <value>74LS04</value>
      <libsource lib="74xx" part="74LS04"/>
      <sheetpath names="/" tstamps="/"/>
      <tstamp>4C6E20A6</tstamp>
    </comp>
    <comp ref="C1">
      <value>CP</value>
      <libsource lib="device" part="CP"/>
      <sheetpath names="/" tstamps="/"/>
      <tstamp>4C6E2094</tstamp>
    </comp>
    <comp ref="R1">
      <value>R</value>
      <libsource lib="device" part="R"/>
      <sheetpath names="/" tstamps="/"/>
      <tstamp>4C6E208A</tstamp>
    </comp>
  </components>
  <libparts>
    <libpart lib="device" part="C">
      <description>Condensateur non polarise</description>
      <footprints>
        <fp>SM*</fp>
       <fp>C?</fp>
       <fp>C1-1</fp>
     </footprints>
     <fields>
       <field name="Reference">C</field>
       <field name="Value">C</field>
     </fields>
     <pins>
       <pin num="1" name="~" type="passive"/>
       <pin num="2" name="~" type="passive"/>
     </pins>
   </libpart>
   <libpart lib="device" part="R">
     <description>Resistance</description>
     <footprints>
       <fp>R?</fp>
       <fp>SM0603</fp>
       <fp>SM0805</fp>
       <fp>R?-*</fp>
       <fp>SM1206</fp>
     </footprints>
     <fields>
       <field name="Reference">R</field>
       <field name="Value">R</field>
     </fields>
     <pins>
       <pin num="1" name="~" type="passive"/>
       <pin num="2" name="~" type="passive"/>
     </pins>
   </libpart>
   <libpart lib="conn" part="CONN_4">
     <description>Symbole general de connecteur</description>
     <fields>
       <field name="Reference">P</field>
       <field name="Value">CONN_4</field>
     </fields>
     <pins>
       <pin num="1" name="P1" type="passive"/>
       <pin num="2" name="P2" type="passive"/>
       <pin num="3" name="P3" type="passive"/>
       <pin num="4" name="P4" type="passive"/>
     </pins>
   </libpart>
   <libpart lib="74xx" part="74LS04">
     <description>Hex Inverseur</description>
     <fields>
       <field name="Reference">U</field>
       <field name="Value">74LS04</field>
     </fields>
     <pins>
       <pin num="1" name="~" type="input"/>
       <pin num="2" name="~" type="output"/>
       <pin num="3" name="~" type="input"/>
       <pin num="4" name="~" type="output"/>
       <pin num="5" name="~" type="input"/>
       <pin num="6" name="~" type="output"/>
       <pin num="7" name="GND" type="power_in"/>
       <pin num="8" name="~" type="output"/>
       <pin num="9" name="~" type="input"/>
       <pin num="10" name="~" type="output"/>
       <pin num="11" name="~" type="input"/>
       <pin num="12" name="~" type="output"/>
       <pin num="13" name="~" type="input"/>
       <pin num="14" name="VCC" type="power_in"/>
     </pins>
   </libpart>
   <libpart lib="74xx" part="74LS74">
     <description>Dual D FlipFlop, Set &amp; Reset</description>
     <docs>74xx/74hc_hct74.pdf</docs>
     <fields>
       <field name="Reference">U</field>
       <field name="Value">74LS74</field>
     </fields>
     <pins>
       <pin num="1" name="Cd" type="input"/>
       <pin num="2" name="D" type="input"/>
       <pin num="3" name="Cp" type="input"/>
       <pin num="4" name="Sd" type="input"/>
       <pin num="5" name="Q" type="output"/>
       <pin num="6" name="~Q" type="output"/>
       <pin num="7" name="GND" type="power_in"/>
       <pin num="8" name="~Q" type="output"/>
       <pin num="9" name="Q" type="output"/>
       <pin num="10" name="Sd" type="input"/>
       <pin num="11" name="Cp" type="input"/>
       <pin num="12" name="D" type="input"/>
       <pin num="13" name="Cd" type="input"/>
       <pin num="14" name="VCC" type="power_in"/>
     </pins>
   </libpart>
 </libparts>
 <libraries>
   <library logical="device">
     <uri>F:\kicad\share\library\device.lib</uri>
   </library>
   <library logical="conn">
     <uri>F:\kicad\share\library\conn.lib</uri>
   </library>
   <library logical="74xx">
     <uri>F:\kicad\share\library\74xx.lib</uri>
   </library>
 </libraries>
 <nets>
    <net code="1" name="GND">
      <node ref="U1" pin="7"/>
      <node ref="C1" pin="2"/>
      <node ref="U2" pin="7"/>
      <node ref="P1" pin="4"/>
    </net>
    <net code="2" name="VCC">
      <node ref="R1" pin="1"/>
      <node ref="U1" pin="14"/>
      <node ref="U2" pin="4"/>
      <node ref="U2" pin="1"/>
      <node ref="U2" pin="14"/>
      <node ref="P1" pin="1"/>
    </net>
    <net code="3" name="">
      <node ref="U2" pin="6"/>
    </net>
    <net code="4" name="">
      <node ref="U1" pin="2"/>
      <node ref="U2" pin="3"/>
    </net>
    <net code="5" name="/SIG_OUT">
      <node ref="P1" pin="2"/>
      <node ref="U2" pin="5"/>
      <node ref="U2" pin="2"/>
    </net>
    <net code="6" name="/CLOCK_IN">
      <node ref="R1" pin="2"/>
      <node ref="C1" pin="1"/>
      <node ref="U1" pin="1"/>
      <node ref="P1" pin="3"/>
    </net>
  </nets>
</export>
## Conversion to a new format:
By applying a filter to this Intermediate Netlist file, one can generate netlists in a lot of others format, and B.O.M.
Because this is a text to text transform, this filter can be easily written using PYTHON or XSLT.
XSLT itself is a an XML language to define transformation for XML.
When using XSLT, Xsltproc program can be used to read an XML file, applies a style-sheet (the “filter”and save the resulting output.
So the used has to create a style-sheet file using XSLT conventions.
The full conversion process is handle by Eeschema, and is transparent.
## XSLT approach:
The XSL Transformations (XSLT) documentation is here:
http://www.w3.org/TR/xslt
### Sample to create a Pads-Pcb netlist file
This format has two sections:
- A footprint list
- A Nets list (grouping pads references by nets)

Here is a style-sheet sample to convert the Intermediate Netlist file to a Pads-Pcb netlist format:

<?xml version="1.0" encoding="ISO-8859-1"?>
<!--XSL style sheet to EESCHEMA Generic Netlist Format to PADS netlist format
    Copyright (C) 2010, SoftPLC Corporation.
    GPL v2.

    How to use:
        https://lists.launchpad.net/kicad-developers/msg05157.html
-->

<!DOCTYPE xsl:stylesheet [
  <!ENTITY nl "&#xd;&#xa;"> <!--new line CR, LF -->
]>

<xsl:stylesheet version="1.0" xmlns:xsl="http://www.w3.org/1999/XSL/Transform">
<xsl:output method="text" omit-xml-declaration="yes" indent="no"/>

<xsl:template match="/export">
    <xsl:text>*PADS-PCB*&nl;*PART*&nl;</xsl:text>
    <xsl:apply-templates select="components/comp"/>
    <xsl:text>&nl;*NET*&nl;</xsl:text>
    <xsl:apply-templates select="nets/net"/>
    <xsl:text>*END*&nl;</xsl:text>
</xsl:template>

<!-- for each component -->
<xsl:template match="comp">
    <xsl:text> </xsl:text>
    <xsl:value-of select="@ref"/>
    <xsl:text> </xsl:text>
    <xsl:choose>
        <xsl:when test = "footprint != '' ">
        <xsl:apply-templates select="footprint"/>
        </xsl:when>
        <xsl:otherwise>
        <xsl:text>unknown</xsl:text>
        </xsl:otherwise>
    </xsl:choose>
    <xsl:text>&nl;</xsl:text>
</xsl:template>

<!-- for each net -->
<xsl:template match="net">
    <!-- nets are output only if there is more than one pin in net -->
    <xsl:if test="count(node)>1">
        <xsl:text>*SIGNAL* </xsl:text>
        <xsl:choose>
        <xsl:when test = "@name != '' ">
        <xsl:value-of select="@name"/>
        </xsl:when>
        <xsl:otherwise>
        <xsl:text>N-</xsl:text>
        <xsl:value-of select="@code"/>
        </xsl:otherwise>
        </xsl:choose>
        <xsl:text>&nl;</xsl:text>
        <xsl:apply-templates select="node"/>
    </xsl:if>
</xsl:template>

<!-- for each node -->
<xsl:template match="node">
    <xsl:text> </xsl:text>
    <xsl:value-of select="@ref"/>
    <xsl:text>.</xsl:text>
    <xsl:value-of select="@pin"/>
    <xsl:text>&nl;</xsl:text>
</xsl:template>

</xsl:stylesheet>

Here is the final output, after applying xsltproc:

*PADS-PCB*
*PART*
P1 unknown
U2 unknown
U1 unknown
C1 unknown
R1 unknown
*NET*
*SIGNAL* GND
U1.7
C1.2
U2.7
P1.4
*SIGNAL* VCC
R1.1
U1.14
U2.4
U2.1
U2.14
P1.1
*SIGNAL* N-4
U1.2
U2.3
*SIGNAL* /SIG_OUT
P1.2
U2.5
U2.2
*SIGNAL* /CLOCK_IN
R1.2
C1.1
U1.1
P1.3
*END*

And the command line to convert the netlist files is:
f:/kicad/bin/xsltproc.exe -o test.net f:/kicad/bin/plugins/netlist_form_pads-pcb.xsl test.tmp
### Sample to create a Cadstar netlist file
This format has two sections:
- A footprint list
- A Nets list (grouping pads references by nets)

#### The Style-Sheet file:

<?xml version="1.0" encoding="ISO-8859-1"?>
<!--XSL style sheet to EESCHEMA Generic Netlist Format to CADSTAR netlist format
    Copyright (C) 2010, Jean-Pierre Charras.
    Copyright (C) 2010, SoftPLC Corporation.
    GPL v2.

<!DOCTYPE xsl:stylesheet [
  <!ENTITY nl "&#xd;&#xa;"> <!--new line CR, LF -->
]>

<xsl:stylesheet version="1.0" xmlns:xsl="http://www.w3.org/1999/XSL/Transform">
<xsl:output method="text" omit-xml-declaration="yes" indent="no"/>

<!-- Netlist header -->
<xsl:template match="/export">
    <xsl:text>.HEA&nl;</xsl:text>
    <xsl:apply-templates select="design/date"/> <!-- Generate line .TIM <time> -->
    <xsl:apply-templates select="design/tool"/> <!-- Generate line .APP <eeschema version> -->
    <xsl:apply-templates select="components/comp"/> <!-- Generate list of components -->
    <xsl:text>&nl;&nl;</xsl:text>
    <xsl:apply-templates select="nets/net"/> <!-- Generate list of nets and connections -->
    <xsl:text>&nl;.END&nl;</xsl:text>
</xsl:template>

 <!-- Generate line .TIM 20/08/2010 10:45:33 -->
<xsl:template match="tool">
    <xsl:text>.APP "</xsl:text>
    <xsl:apply-templates/>
    <xsl:text>"&nl;</xsl:text>
</xsl:template>

 <!-- Generate line .APP "eeschema (2010-08-17 BZR 2450)-unstable" -->
<xsl:template match="date">
    <xsl:text>.TIM </xsl:text>
    <xsl:apply-templates/>
    <xsl:text>&nl;</xsl:text>
</xsl:template>

<!-- for each component -->
<xsl:template match="comp">
    <xsl:text>.ADD_COM </xsl:text>
    <xsl:value-of select="@ref"/>
    <xsl:text> </xsl:text>
    <xsl:choose>
        <xsl:when test = "value != '' ">
        <xsl:text>"</xsl:text> <xsl:apply-templates select="value"/> <xsl:text>"</xsl:text>
        </xsl:when>
        <xsl:otherwise>
        <xsl:text>""</xsl:text>
        </xsl:otherwise>
    </xsl:choose>
    <xsl:text>&nl;</xsl:text>
</xsl:template>

<!-- for each net -->
<xsl:template match="net">
    <!-- nets are output only if there is more than one pin in net -->
    <xsl:if test="count(node)>1">
    <xsl:variable name="netname">
        <xsl:text>"</xsl:text>
        <xsl:choose>
        <xsl:when test = "@name != '' ">
        <xsl:value-of select="@name"/>
        </xsl:when>
        <xsl:otherwise>
        <xsl:text>N-</xsl:text>
        <xsl:value-of select="@code"/>
        </xsl:otherwise>
        </xsl:choose>
        <xsl:text>"&nl;</xsl:text>
        </xsl:variable>
        <xsl:apply-templates select="node" mode="first"/>
        <xsl:value-of select="$netname"/>
        <xsl:apply-templates select="node" mode="others"/>
    </xsl:if>
</xsl:template>

<!-- for each node -->
<xsl:template match="node" mode="first">
    <xsl:if test="position()=1">
       <xsl:text>.ADD_TER </xsl:text>
    <xsl:value-of select="@ref"/>
    <xsl:text>.</xsl:text>
    <xsl:value-of select="@pin"/>
    <xsl:text> </xsl:text>
    </xsl:if>
</xsl:template>

<xsl:template match="node" mode="others">
    <xsl:choose>
        <xsl:when test='position()=1'>
        </xsl:when>
        <xsl:when test='position()=2'>
        <xsl:text>.TER </xsl:text>
        </xsl:when>
        <xsl:otherwise>
        <xsl:text> </xsl:text>
        </xsl:otherwise>
    </xsl:choose>
    <xsl:if test="position()>1">
        <xsl:value-of select="@ref"/>
        <xsl:text>.</xsl:text>
        <xsl:value-of select="@pin"/>
        <xsl:text>&nl;</xsl:text>
    </xsl:if>
</xsl:template>

</xsl:stylesheet>

#### The output file:
.HEA
.TIM 21/08/2010 08:12:08
.APP "eeschema (2010-08-09 BZR 2439)-unstable"
.ADD_COM P1 "CONN_4"
.ADD_COM U2 "74LS74"
.ADD_COM U1 "74LS04"
.ADD_COM C1 "CP"
.ADD_COM R1 "R"

.ADD_TER U1.7 "GND"
.TER C1.2
        U2.7
        P1.4
.ADD_TER R1.1 "VCC"
.TER U1.14
        U2.4
        U2.1
        U2.14
        P1.1
.ADD_TER U1.2 "N-4"
.TER U2.3
.ADD_TER P1.2 "/SIG_OUT"
.TER U2.5
        U2.2
.ADD_TER R1.2 "/CLOCK_IN"
.TER C1.1
        U1.1
        P1.3

.END

### Sample to create a OrcadPCB2 netlist file
This format has only one section: the footprint list:
Each footprint includes its list of pads with reference to a net.
#### The Style-Sheet file:

<?xml version="1.0" encoding="ISO-8859-1"?>
<!--XSL style sheet to EESCHEMA Generic Netlist Format to CADSTAR netlist format
    Copyright (C) 2010, SoftPLC Corporation.
    GPL v2.

    How to use:
        https://lists.launchpad.net/kicad-developers/msg05157.html
-->

<!DOCTYPE xsl:stylesheet [
  <!ENTITY nl "&#xd;&#xa;"> <!--new line CR, LF -->
]>

<xsl:stylesheet version="1.0" xmlns:xsl="http://www.w3.org/1999/XSL/Transform">
<xsl:output method="text" omit-xml-declaration="yes" indent="no"/>

<!--
    Netlist header
    Creates the entire netlist
    (can be seen as equivalent to main function in C
-->
<xsl:template match="/export">
    <xsl:text>( { EESchema Netlist Version 1.1 </xsl:text>
    <!-- Generate line .TIM <time> -->
    <xsl:apply-templates select="design/date"/>
    <!-- Generate line eeschema version ... -->
    <xsl:apply-templates select="design/tool"/>
    <xsl:text>}&nl;</xsl:text>

    <!-- Generate the list of components -->
    <xsl:apply-templates select="components/comp"/> <!-- Generate list of components -->

    <!-- end of file -->
    <xsl:text>)&nl;*&nl;</xsl:text>
</xsl:template>

<!--
    Generate id in header like "eeschema (2010-08-17 BZR 2450)-unstable"
-->
<xsl:template match="tool">
    <xsl:apply-templates/>
</xsl:template>

<!--
    Generate date in header like "20/08/2010 10:45:33"
-->
<xsl:template match="date">
    <xsl:apply-templates/>
    <xsl:text>&nl;</xsl:text>
</xsl:template>

<!--
    This template read each component
    (path = /export/components/comp)
    creates lines:
     ( 3EBF7DBD $noname U1 74LS125
      ... pin list ...
      )
    and calls "create_pin_list" template to build the pin list
-->
<xsl:template match="comp">
    <xsl:text> ( </xsl:text>
    <xsl:choose>
        <xsl:when test = "tstamp != '' ">
        <xsl:apply-templates select="tstamp"/>
        </xsl:when>
        <xsl:otherwise>
        <xsl:text>00000000</xsl:text>
        </xsl:otherwise>
    </xsl:choose>
    <xsl:text> </xsl:text>
    <xsl:choose>
        <xsl:when test = "footprint != '' ">
        <xsl:apply-templates select="footprint"/>
        </xsl:when>
        <xsl:otherwise>
        <xsl:text>$noname</xsl:text>
        </xsl:otherwise>
    </xsl:choose>
    <xsl:text> </xsl:text>
    <xsl:value-of select="@ref"/>
    <xsl:text> </xsl:text>
    <xsl:choose>
        <xsl:when test = "value != '' ">
        <xsl:apply-templates select="value"/>
        </xsl:when>
        <xsl:otherwise>
        <xsl:text>"~"</xsl:text>
        </xsl:otherwise>
    </xsl:choose>
    <xsl:text>&nl;</xsl:text>
    <xsl:call-template name="Search_pin_list" >
        <xsl:with-param name="cmplib_id" select="libsource/@part"/>
        <xsl:with-param name="cmp_ref" select="@ref"/>
    </xsl:call-template>
    <xsl:text> )&nl;</xsl:text>
</xsl:template>

<!--
    This template search for a given lib component description in list
    lib component descriptions are in /export/libparts,
    and each description start at ./libpart
    We search here for the list of pins of the given component
    This template has 2 parameters:
        "cmplib_id" (reference in libparts)
        "cmp_ref" (schematic reference of the given component)
-->
<xsl:template name="Search_pin_list" >
    <xsl:param name="cmplib_id" select="0" />
    <xsl:param name="cmp_ref" select="0" />
        <xsl:for-each select="/export/libparts/libpart">
        <xsl:if test = "@part = $cmplib_id ">
        <xsl:apply-templates name="build_pin_list" select="pins/pin">
        <xsl:with-param name="cmp_ref" select="$cmp_ref"/>
        </xsl:apply-templates>
        </xsl:if>
        </xsl:for-each>
</xsl:template>

<!--
    This template writes the pin list of a component
    from the pin list of the library description
    The pin list from library description is something like
        <pins>
        <pin num="1" type="passive"/>
        <pin num="2" type="passive"/>
        </pins>
    Output pin list is ( <pin num> <net name> )
    something like
        ( 1 VCC )
        ( 2 GND )
-->
<xsl:template name="build_pin_list" match="pin">
    <xsl:param name="cmp_ref" select="0" />

    <!-- write pin numner and separator -->
    <xsl:text> ( </xsl:text>
    <xsl:value-of select="@num"/>
    <xsl:text> </xsl:text>

    <!-- search net name in nets section and write it: -->
    <xsl:variable name="pinNum" select="@num" />
    <xsl:for-each select="/export/nets/net">
        <!-- net name is output only if there is more than one pin in net
        else use "?" as net name, so count items in this net
        -->
        <xsl:variable name="pinCnt" select="count(node)" />
        <xsl:apply-templates name="Search_pin_netname" select="node">
        <xsl:with-param name="cmp_ref" select="$cmp_ref"/>
        <xsl:with-param name="pin_cnt_in_net" select="$pinCnt"/>
        <xsl:with-param name="pin_num"> <xsl:value-of select="$pinNum"/>
        </xsl:with-param>
        </xsl:apply-templates>
    </xsl:for-each>

    <!-- close line -->
    <xsl:text> )&nl;</xsl:text>
</xsl:template>

<!--
    This template writes the pin netname of a given pin of a given component
    from the nets list
    The nets list description is something like
      <nets>
        <net code="1" name="GND">
        <node ref="J1" pin="20"/>
        <node ref="C2" pin="2"/>
        </net>
        <net code="2" name="">
        <node ref="U2" pin="11"/>
        </net>
    </nets>
    This template has 2 parameters:
        "cmp_ref" (schematic reference of the given component)
        "pin_num" (pin number)
-->

<xsl:template name="Search_pin_netname" match="node">
    <xsl:param name="cmp_ref" select="0" />
    <xsl:param name="pin_num" select="0" />
    <xsl:param name="pin_cnt_in_net" select="0" />

    <xsl:if test = "@ref = $cmp_ref ">
        <xsl:if test = "@pin = $pin_num">
        <!-- net name is output only if there is more than one pin in net
        else use "?" as net name
        -->
        <xsl:if test = "$pin_cnt_in_net>1">
        <xsl:choose>
        <!-- if a net has a name, use it,
        else build a name from its net code
        -->
        <xsl:when test = "../@name != '' ">
        <xsl:value-of select="../@name"/>
        </xsl:when>
        <xsl:otherwise>
        <xsl:text>$N-0</xsl:text><xsl:value-of select="../@code"/>
        </xsl:otherwise>
        </xsl:choose>
        </xsl:if>
        <xsl:if test = "$pin_cnt_in_net &lt;2">
        <xsl:text>?</xsl:text>
        </xsl:if>
        </xsl:if>
    </xsl:if>

</xsl:template>

</xsl:stylesheet>

#### The output file:

( { EESchema Netlist Version 1.1 29/08/2010 21:07:51
eeschema (2010-08-28 BZR 2458)-unstable}
 ( 4C6E2141 $noname P1 CONN_4
  ( 1 VCC )
  ( 2 /SIG_OUT )
  ( 3 /CLOCK_IN )
  ( 4 GND )
 )
 ( 4C6E20BA $noname U2 74LS74
  ( 1 VCC )
  ( 2 /SIG_OUT )
  ( 3 N-04 )
  ( 4 VCC )
  ( 5 /SIG_OUT )
  ( 6 ? )
  ( 7 GND )
  ( 14 VCC )
 )
 ( 4C6E20A6 $noname U1 74LS04
  ( 1 /CLOCK_IN )
  ( 2 N-04 )
  ( 7 GND )
  ( 14 VCC )
 )
 ( 4C6E2094 $noname C1 CP
  ( 1 /CLOCK_IN )
  ( 2 GND )
 )
 ( 4C6E208A $noname R1 R
  ( 1 VCC )
  ( 2 /CLOCK_IN )
 )
)
*

### Using Eeschema plugins interface:
Intermediate Netlist converters can be automatically launched by Eeschema
#### Init the Dialog window:
One can add a new netlist plug-in by « Add Plugin »

Here is the plug-in « PadsPcb » setup:
Windows:

Linux:

Because this intermediate file contains most of info about components, a BOM can be extracted from ithis file.
Here is the plug-in setup to create a customized Bill Of Material (BOM):
Windows:

#### Parameters:
The setup needs:
- A title (for instance: the name of the netlist format)
- The command line to launch the converter.
On activate the Netlist button:
1. Eeschema creates an intermediate netlist file *.xml, for instance test.xml
2. Eeschema runs the plug-in, what read test.xml and creates test.net
#### The command line:
Assuming we are using xsltproc.exe to apply the sheet style to the intermediate file:
xsltproc.exe needs a command like:
xsltproc.exe -o <output filename> < style-sheet filename> <input XML file to convert>
So, in Kicad the command line is (using Windows):
“f:/kicad/bin/xsltproc.exe” -o “%O” “f:/kicad/bin/plugins/netlist_form_pads-pcb.xsl” “%I”
or (using Linux)
xsltproc -o “%O” “/usr/local/kicad/bin/plugins/netlist_form_pads-pcb.xsl” “%I”
netlist_form_pads-pcb.xsl is the style-sheet.
Do not forget to quote file names if they have spaces in name.
#### Command line format:
<path of xsltproc >xsltproc < xsltproc parameters>
For parameters, supported formatting sequences are:
- %B => base filename and path of selected output file, minus path and extension.
- %I => complete filename and path of the temporary input file.
- %O => complete filename and path of the user chosen output file.
%I will be replaced by the actual intermediate file name
%O will be replaced by the actual output file name (the final netlist file)
And a command line could be
- under Windows:
  f:/kicad/bin/xsltproc.exe -o %O f:/kicad/bin/plugins/netlist_form_pads-pcb.xsl %I
- under Linux)
  xsltproc -o %O /usr/local/kicad/bin/plugins/netlist_form_pads-pcb.xsl %I
Assuming xsltproc is installed on your PC b(under Windows, all files in kicad/bin).
## The Intermediate Netlist structure:
This sample gives an idea of the file.
<?xml version="1.0" encoding="utf-8"?>
<export version="D">
  <design>
    <source>F:\kicad_aux\netlist_test\netlist_test.sch</source>
    <date>29/08/2010 21:07:51</date>
    <tool>eeschema (2010-08-28 BZR 2458)-unstable</tool>
  </design>
  <components>
    <comp ref="P1">
      <value>CONN_4</value>
      <libsource lib="conn" part="CONN_4"/>
      <sheetpath names="/" tstamps="/"/>
      <tstamp>4C6E2141</tstamp>
    </comp>
    <comp ref="U2">
      <value>74LS74</value>
      <libsource lib="74xx" part="74LS74"/>
      <sheetpath names="/" tstamps="/"/>
      <tstamp>4C6E20BA</tstamp>
    </comp>
    <comp ref="U1">
      <value>74LS04</value>
      <libsource lib="74xx" part="74LS04"/>
      <sheetpath names="/" tstamps="/"/>
      <tstamp>4C6E20A6</tstamp>
    </comp>
    <comp ref="C1">
      <value>CP</value>
      <libsource lib="device" part="CP"/>
      <sheetpath names="/" tstamps="/"/>
      <tstamp>4C6E2094</tstamp>
    <comp ref="R1">
      <value>R</value>
      <libsource lib="device" part="R"/>
      <sheetpath names="/" tstamps="/"/>
      <tstamp>4C6E208A</tstamp>
    </comp>
  </components>
  <libparts/>
  <libraries/>
  <nets>
    <net code="1" name="GND">
      <node ref="U1" pin="7"/>
      <node ref="C1" pin="2"/>
      <node ref="U2" pin="7"/>
      <node ref="P1" pin="4"/>
    </net>
    <net code="2" name="VCC">
      <node ref="R1" pin="1"/>
      <node ref="U1" pin="14"/>
      <node ref="U2" pin="4"/>
      <node ref="U2" pin="1"/>
      <node ref="U2" pin="14"/>
      <node ref="P1" pin="1"/>
    </net>
    <net code="3" name="">
      <node ref="U2" pin="6"/>
    </net>
    <net code="4" name="">
      <node ref="U1" pin="2"/>
      <node ref="U2" pin="3"/>
    </net>
    <net code="5" name="/SIG_OUT">
      <node ref="P1" pin="2"/>
      <node ref="U2" pin="5"/>
      <node ref="U2" pin="2"/>
    </net>
    <net code="6" name="/CLOCK_IN">
      <node ref="R1" pin="2"/>
      <node ref="C1" pin="1"/>
      <node ref="U1" pin="1"/>
      <node ref="P1" pin="3"/>
    </net>
  </nets>
</export>

### General structure:
The intermediate Netlist has 5 sections:
- the header section.
- The component section.
- The lib parts section.
- The libraries section.
- The nets section.
The whole file has the delimiter <export>

<export version="D">
 ...
</export>
### The header section:
The header has the delimiter <design>

  <design>
    <source>F:\kicad_aux\netlist_test\netlist_test.sch</source>
    <date>21/08/2010 08:12:08</date>
    <tool>eeschema (2010-08-09 BZR 2439)-unstable</tool>
  </design>

This section can be seen as comments.
### The components section:
The component section has the delimiter <components>

  <components>
    <comp ref="P1">
      <value>CONN_4</value>
      <libsource lib="conn" part="CONN_4"/>
      <sheetpath names="/" tstamps="/"/>
      <tstamp>4C6E2141</tstamp>
    </comp>
  </components>

This is the list of components in schematic.
Each component is described like this:

    <comp ref="P1">
      <value>CONN_4</value>
      <libsource lib="conn" part="CONN_4"/>
      <sheetpath names="/" tstamps="/"/>
      <tstamp>4C6E2141</tstamp>
    </comp>

libsource	name of the lib where this component was found.
part	component name inside this library.
sheetpath	« path » of the sheet inside the hierarchy: identify the sheet within the full schematic hierarchy.
tstamps (time stamps)	time stamp of the schematic file.
tstamp (time stamp)	time stamp of the component.

#### Note about time stamps for components:
To identify a component in a netlist (and therefore on a board), the reference is used, and is unique for each component.
However Kicad provides an auxiliary way to identify a component, and its corresponding footprint on the board.
This allows the re-annotation of components in a schematic project and do not loose the link between the component and its footprint.
A time stamp is an unique identifier for each component or sheet in a schematic project.
However, in complex hierarchies, the same sheet is used more than once, so this sheet contains components having the same time stamp.
A given sheet (inside a complex hierarchy) has an unique identifier: its sheetpath.
A given component (inside a complex hierarchy) has an unique identifier: the sheetpath+its tstamp
### The libparts section:
The libparts section has the delimiter <libparts>, and the data in this section is defined in the schematic libraries
Its contains for each component:
- The allowed footprints names (names use jokers) delimiter <fp>
- The fields defined in the library delimiter <fields>.
- The list of pins delimiter <pins>

  <libparts>
    <libpart lib="device" part="CP">
      <description>Condensateur polarise</description>
      <footprints>
        <fp>CP*</fp>
        <fp>SM*</fp>
      </footprints>
      <fields>
        <field name="Reference">C</field>
        <field name="Valeur">CP</field>
      </fields>
      <pins>
        <pin num="1" name="1" type="passive"/>
        <pin num="2" name="2" type="passive"/>
      </pins>
    </libpart>
  </libparts>

Lines like <pin num="1" type="passive"/> give also the electrical pin type.
Electrical pin types are:
Input	Usual input pin
Output	Usual output
Bidirectional	Input or Output
Tri-state	Bus input/output
Passive	Usual ends of passive components
Unspecified	Unknown electrical type
Power input	Power input of a component
Power output	Power output like a regulator output
Open collector	Open collector often found in analog comparators
Open emitter	Open collector sometimes found in logic.
Not connected	Must be left open in schematic

### The libraries section:
The libraries section has the delimiter <libraries>
Gives the list of schematic libraries used in the schematic project.
  <libraries>
    <library logical="device">
      <uri>F:\kicad\share\library\device.lib</uri>
    </library>
    <library logical="conn">
      <uri>F:\kicad\share\library\conn.lib</uri>
    </library>
  </libraries>

### The nets section:
The nets section has the delimiter <nets>.
This is the connectivity of the schematic.

  <nets>
    <net code="1" name="GND">
      <node ref="U1" pin="7"/>
      <node ref="C1" pin="2"/>
      <node ref="U2" pin="7"/>
      <node ref="P1" pin="4"/>
    </net>
    <net code="2" name="VCC">
      <node ref="R1" pin="1"/>
      <node ref="U1" pin="14"/>
      <node ref="U2" pin="4"/>
      <node ref="U2" pin="1"/>
      <node ref="U2" pin="14"/>
      <node ref="P1" pin="1"/>
    </net>
  </nets>

This sections lists all nets in the schematic.
A given net is :
    <net code="1" name="GND">
      <node ref="U1" pin="7"/>
      <node ref="C1" pin="2"/>
      <node ref="U2" pin="7"/>
      <node ref="P1" pin="4"/>
    </net>

net code	is an internal identifier for this net
name	is a name for this net
node	give a pin reference connected to this net

## More info about xsltproc:
See http://xmlsoft.org/XSLT/xsltproc.html

### Introduction
xsltproc is a command line tool for applying XSLT stylesheets to XML documents.
It is part of libxslt, the XSLT C library for GNOME.
While it was developed as part of the GNOME project, it can operate independently of the GNOME desktop.
xsltproc is invoked from the command line with the name of the stylesheet to be used followed by the name of the file or files to which the stylesheet is to be applied. It will use the standard input if a filename provided is - .
If a stylesheet is included in an XML document with a Stylesheet Processing Instruction, no stylesheet need be named at the command line. xsltproc will automatically detect the included stylesheet and use it.
By default, output is to stdout. You can specify a file for output using the -o option.
### Synopsis
xsltproc [[-V] | [-v] | [-o file] | [--timing] | [--repeat] | [--debug] | [--novalid] | [--noout] | [--maxdepth val] | [--html] | [--param name value] | [--stringparam name value] | [--nonet] | [--path paths] | [--load-trace] | [--catalogs] | [--xinclude] | [--profile] | [--dumpextensions] | [--nowrite] | [--nomkdir] | [--writesubtree] | [--nodtdattr]] [stylesheet] [file1] [file2] [....]
### Command Line Options
-V or --version
Show the version of libxml and libxslt used.
-v or --verbose
Output each step taken by xsltproc in processing the stylesheet and the document.
-o or --output file
Direct output to the file named file. For multiple outputs, also known as "chunking", -o directory/ directs the output files to a specified directory. The directory must already exist.
--timing
Display the time used for parsing the stylesheet, parsing the document and applying the stylesheet and saving the result. Displayed in milliseconds.
--repeat
Run the transformation 20 times. Used for timing tests.
--debug
Output an XML tree of the transformed document for debugging purposes.
--novalid
Skip loading the document's DTD.
--noout
Do not output the result.
--maxdepth value
Adjust the maximum depth of the template stack before libxslt concludes it is in an infinite loop. The default is 500.
--html
The input document is an HTML file.
--param name value
Pass a parameter of name name and value value to the stylesheet. You may pass multiple name/value pairs up to a maximum of 32. If the value being passed is a string rather than a node identifier, use --stringparam instead.
--stringparam name value
Pass a paramenter of name name and value value where value is a string rather than a node identifier. (Note: The string must be utf-8.)
--nonet
Do not use the Internet to fetch DTD's, entities or documents.
--path paths
Use the list (separated by space or column) of filesystem paths specified by paths to load DTDs, entities or documents.
--load-trace
Display to stderr all the documents loaded during the processing.
--catalogs
Use the SGML catalog specified in SGML_CATALOG_FILES to resolve the location of external entities. By default, xsltproc looks for the catalog specified in XML_CATALOG_FILES. If that is not specified, it uses /etc/xml/catalog.
--xinclude
Process the input document using the Xinclude specification. More details on this can be found in the Xinclude specification: http://www.w3.org/TR/xinclude/
--profile or --norman
Output profiling information detailing the amount of time spent in each part of the stylesheet. This is useful in optimizing stylesheet performance.
--dumpextensions
Dumps the list of all registered extensions on stdout.
--nowrite
Refuses to write to any file or resource.
--nomkdir
Refuses to create directories.
--writesubtree path
Allow file write only within the path subtree.
--nodtdattr
Do not apply default attributes from the document's DTD.
### Return values
xsltproc's return codes provide information that can be used when calling it from scripts.
0: normal
1: no argument
2: too many parameters
3: unknown option
4: failed to parse the stylesheet
5: error in the stylesheet
6: error in one of the documents
7: unsupported xsl:output method
8: string parameter contains both quote and double-quotes
9: internal processing error
10: processing was stopped by a terminating message
11: could not write the result to the output file
### More Information
libxml web page: http://www.xmlsoft.org/
W3C XSLT page: http://www.w3.org/TR/xslt